## Slide 1: The Functional Mockup Interface for Tool independent Exchange of Simulation Models
Torsten Blochwitz (ITI), Martin Otter (DLR-RM)
M. Arnold University of Halle
C. Bausch, M. Monteiro Atego Systems GmbH
C. Clauß, S. Wolf Fraunhofer IIS EAS, Dresden
H. Elmqvist, H. Olsson Dassault Systèmes, Lund
A. Junghanns, J. Mauss QTronic, Berlin
T. Neidhold ITI, Dresden,
D. Neumerkel Daimler AG, Stuttgart
J.-V. Peetz Fraunhofer SCAI, St. Augustin
Modelica 2011, 21st,22nd March

## Slide 2: Functional Mock-up Interface (FMI) - Motivation (1)
Problems / Needs
Component development by supplier
Integration by OEM
Many different simulation tools
?
supplier1
supplier2
supplier3
supplier4
supplier5
OEM
supplier1
tool 1
supplier2
supplier3
supplier4
supplier5
tool 2
tool 3
tool 4
tool 5
FMI
OEM
Solution
Reuse of supplier models by OEM:
  DLL (model import) and/or
  Tool coupling (co-simulation)
Protection of model IP of supplier
!
supplier1
supplier2
supplier3
OEM
Added Value
Early validation of design
Increased process efficiency and quality
slide from Nick Suyam, Daimler (adapted)

## Slide 3: FMI - Motivation (2)
No standards available for:
  Model interface based on C or binaries
  Co-simulation between simulation tools
Lots of proprietary interfaces:
  Simulink: S-function
  Modelica: external function, external object interface
  QTronic Silver: Silver-Module API
  SimulationX: External Model Interface
  NI LabVIEW: External Model Interface, Simulation Interface Toolkit
  Simpack: uforce routines
  ADAMS: user routines
  …

## Slide 4: FMI – Overview
The FMI development is part of the ITEA2 MODELISAR project (2008 - 2011; 29 partners, Budget: 30 Mill. €)
FMI development initiated, organized and headed by Daimler AG
Improved Software/Model/Hardware-in-the-Loop Simulation, of physical models from different vendors.
Open Standard
14 Automotive Use-Cases to evaluate FMI.
Engine with ECU
Gearbox with ECU
Thermal systems
Automated cargo door
Chassis components, roadway, ECU (e.g. ESP)
etc.
functional mockup interface for model exchange and tool coupling
courtesy Daimler

## Slide 5: FMI - Main Design Idea (1)
FMI for Model Exchange:
    Version 1.0 released in January 2010
FMI for Co-Simulation:
  Reuses as much as possible from FMI for Model Exchange standard
  Version 1.0 released in October 2010
Tool
Solver
FMU
Model
Tool
FMU
Model
Solver

## Slide 6: FMI - Main Design Idea (2)
A component which implements the interface is called Functional Mockup Unit (FMU)
Separation of
  Description of interface data (XML file)
  Functionality (C code or binary)
A FMU is a zipped file (*.fmu) containing the XML description file and the implementation in source or binary form
Additional data and functionality can be included
Interface specification: www.functional-mockup-interface.org

## Slide 7
XML schema (.xsd)
defined by the
FMI specification

## Slide 8: FMI XML Schema
Information not needed for execution is stored in one xml-file:
  Complex data structures give still simple interface.
  Reduced overhead in terms of memory.
Variable names and attributes
Definition of display units
Definition of type defaults
Default stop time, tol. etc.
Tool specific data

## Slide 9: Example
<?xml version="1.0" encoding="UTF8"?>
<fmiModelDescription
fmiVersion="1.0"
modelName="Modelica.Mechanics.Rotational.Examples.Friction"
modelIdentifier="Modelica_Mechanics_Rotational_Examples_Friction"
guid="{8c4e810f-3df3-4a00-8276-176fa3c9f9e0}"
...
numberOfContinuousStates="6"
numberOfEventIndicators="34"/>
<UnitDefinitions>
<BaseUnit unit="rad">
<DisplayUnitDefinition displayUnit="deg" gain="57.2957795130823"/>
</BaseUnit>
</UnitDefinitions>
<TypeDefinitions>
<Type name="Modelica.SIunits.AngularVelocity">
<RealType quantity="AngularVelocity" unit="rad/s"/>
</Type>
</TypeDefinitions>
<ModelVariables>
<ScalarVariable
name="inertia1.J"
valueReference="16777217"
description="Moment of inertia"
variability="parameter">
<Real declaredType="Modelica.SIunits.Torque" start="1"/>
</ScalarVariable>
...
</ModelVariables>
</fmiModelDescription>
modelDescription.xml

## Slide 10: C-Interface
Two C-header files:
  Platform dependent definitions (basic types):
  C-functions:
    18 core functions
    6 utility functions
    no macros
    C-function name: <ModelIdentifier>_<name>, e.g. Drive_fmiSetTime"

## Slide 11: C-Interface
Instantiation: fmiComponent fmiInstantiateXXX(fmiString instanceName, ...)
Returns an instance of the FMU. Returned fmiComponent is a parameter of the other interface functions. It is of type void* for the master. The FMU uses it to hold all necessary information.
Functions for initialization, termination, destruction
Support of real, integer, boolean, and string inputs, outputs, parameters
Set and Get functions for each type: fmiStatus fmiSetReal (fmiComponent c, const fmiValueReference vr[], size_t nvr, const fmiReal value[]) fmiStatus fmiSetInteger(fmiComponent c, const fmiValueReference vr[], size_t nvr, const fmiInteger value[])
Identification by valueReference, defined in the XML description file for each variable

## Slide 12: FMI for Model Exchange (1)
Import and export of input/output blocks (FMU – Functional Mock-up Unit)
described by
  differential-, algebraic-, discrete equations,
  with time-, state, and step-events
FMU can be large (e.g. 100000 variables)
FMU can be used in an embedded system (small overhead)
FMUs can be connected together

## Slide 13: FMI for Model Exchange
For example: 10 input/output signals (u/y) for connection and 100000 internal variables (v) for plotting
Signals of an FMU

## Slide 14
// Set input arguments fmiSetTime(m, time); fmiSetReal(m, id_u1, u1, nu1); fmiSetContinuousStates(m, x, nx); // Get results fmiGetContinuousStates(m, derx, nx); fmiGetEventIndicators (m, z, nz);
Example:

## Slide 15: Co-Simulation
Definition:
  Coupling of several simulation tools
  Each tool treats one part of a modular coupled problem
  Data exchange is restricted to discrete communication points
  Subsystems are solved independently between communication points
Motivation:
  Simulation of heterogeneous systems
  Partitioning and parallelization of large systems
  Multirate integration
  Hardware-in-the-loop simulation

## Slide 16: FMI for Co-Simulation
Master/slave architecture
Considers different capabilities of simulation tools
Support of simple and sophisticated coupling algorithms:
  Iterative and straight forward algorithms
  Constant and variable communication step size
Allows (higher order) interpolation of continuous inputs
Support of local and distributed co-simulation scenarios
FMI for Co-Simulation does not define:
  Co-simulation algorithms
  Communication technology for distributed scenarios

## Slide 17: FMI for Co-Simulation
Signals of an FMU for Co-Simulation
  Inputs, outputs, and parameters, status information
  Derivatives of inputs, outputs w.r.t. time can be set/retreived for supporting of higher order approximation
u
y
Enclosing Model
v
Solver
x
t
External Model (FMU instance)
Co-Simulation Slave (FMU instance)
t
Model
Solver
Co-Simulation Master
t0, p

## Slide 18: FMI for Co-Simulation C-Interface
Execution of a time step: fmiStatus fmiDoStep(fmiComponent c, fmiReal currentCommunicationPoint, fmiReal communicationStepSize, fmiBoolean newStep)
communicationStepSize can be zero in case of event iteration
newStep = fmiTrue if last step was accepted by the master
It depends on the capabilities of the slave which parameter constellations and calling sequences are allowed
Depending on internal state of the slave and the function parameters, slave can decide which action is to be done before the computation
Return values are fmiOK, fmiDiscard, fmiError, fmiPending
Asynchronous execution is possible

## Slide 19: FMI for Co-Simulation Use Case
Co-Simulation stand alone:
Co-Simulation tool:
Process
Executable
Library (DLL)
Slave
Model
Solver
Slave
Model
Solver
Master
Process 1
Executable
Library (DLL)
Process 2
Simulation tool
Slave
Model
Solver
FMI Wrapper
FMI Wrapper
FMI Wrapper
FMI Wrapper
Master

## Slide 20: FMI for Co-Simulation Use Case
Distributed co-simulation scenario
Data exchange is handled by a communication layer which is implemented by a special FMI wrapper
Master and slave utilize FMI for Co-Simulation only

## Slide 21: Tools supporting FMI (from FMI web site)

## Slide 22: Conclusions and Outlook
FMI has a high potential being widely accepted in the CAE world:
  Initiated, organized and pushed by Daimler to significantly improve the exchange of simulation models between suppliers and OEMs.
  Defined in close collaboration of different tool vendors.
  Industrial users were involved in the proof of concept.
  FMI can already be used with several Modelica tools, Simulink, multi-body and other tools.
FMI is maintained and further developed:
  Unification and harmonization of FMI for Model Exchange and Co‑Simulation (FMI 2.0) within Modelisar.
  Improved handling of time events.
  Clean handling of changeable parameters.
  Efficient interface to Jacobian matrices.

## Slide 23: Acknowledgments
FMI initiated and organized: Daimler AG (Bernd Relovsky, ....)
Head of FMI development: Dietmar Neumerkel (Daimler AG)
Head of FMI-for-Model-Exchange: Martin Otter (DLR-RM)
FMI-for-Model-Exchange Torsten Blochwitz (ITI) Core-Design by: Hilding Elmqvist (Dassault Systèmes -Dynasim) Andreas Junghanns (QTronic) Jakob Mauss (QTronic) Hans Olsson (Dassault Systèmes -Dynasim) Martin Otter (DLR-RM)
Other MODELISAR contributors: Ingrid Bausch-Gall, Bausch-Gall GmbH Alex Eichberger, SIMPACK AG Rainer Keppler, SIMPACK AG Gerd Kurzbach, ITI GmbH Carsten Kübler, TWT Johannes Mezger, TWT Thomas Neidhold, ITI GmbH Dietmar Neumerkel, Daimler AG Peter Nilsson, Dassault Systèmes-Dynasim Antoine Viel, LMS International Daniel Weil, Dassault Systèmes
Other contributors: Johan Akesson, Lund University Joel Andersson, KU Leuven Roberto Parrotto, Politecnico di Milano

## Slide 24: Acknowledgments
FMI for Co-Simulation Martin Arnold, University Halle, Germany
Core-Design by: Constanze Bausch, Atego Systems GmbH, Wolfsburg, Germany
Torsten Blochwitz, ITI GmbH, Dresden, Germany
Christoph Clauß, Fraunhofer IIS EAS, Dresden, Germany
Manuel Monteiro, Atego Systems GmbH, Wolfsburg, Germany
Thomas Neidhold, ITI GmbH, Dresden, Germany
Jörg-Volker Peetz, Fraunhofer SCAI, St. Augustin, Germany
Susann Wolf, Fraunhofer IIS EAS, Dresden, Germany
Contributors: Jens Bastian, Fraunhofer IIS EAS, Dresden, Germany
Christoph Clauß, Fraunhofer IIS EAS, Dresden, Germany
Dietmar Neumerkel, Daimler AG, Böblingen, Germany
Martin Otter, DLR, Oberpfaffenhofen, Germany
Tom Schierz, University Halle, Germany
Wolfgang Trautenberg, Simpack AG, Germany
Klaus Wolf, Fraunhofer SCAI, St. Augustin, Germany
Partially funded by: BMBF, VINNOVA, DGCIS, organized by ITEA2